Linux Networking Tools
Networking Basics

---
- MAC Address
- TCP/IP, Netmask
- DNS
- DHCP
- Gateway, Default route
- Networking protocols

---
- mtr
- ping / fping
- traceroute / tracepath
- wireshark
- tcpdump
- Dig / drill / nslookup / host
- Ifconfig / iwconfig
- Arp-scan
- Nmap
- wpa_supplicant
- netcat
Iftop
Netstat
Tmux
Ssh
Telnet
Route
Resolve.conf
/etc/hosts
Whatmask / sipcalc
Tftp / ftp / sftp
Vnc
Samba
Unbound / bind / nsd
Dhclient / dhcpd
Dhcp (server)
openvpn

---
- Ping
  - Sends ICMP packet
  - Does not recognize ports
  - Useful for verifying basic network connectivity and latency
- Fping
  - Similar to ping, allows multiple simultaneous pings

---
- Traceroute
  - Identifies networking path
- Tracepath
  - Newest version of traceroute included with many linux distros
  - Allows use without root privaledge
- Dig / drill / nslookup / host
  - DNS lookup
  - Try each tool to see which one you like best.
  - Drill is an updated version of dig

---
- Ifconfig
  - Gives IP address and MAC address information
  - Can enable / disable ports
  - BSD version allows near full control of the interface and control of wireless devices
- Iwconfig
  - Similar to ifconfig for wireless devices
  - Allows scanning of nearby access points
- Wpa_supplicant
  - Assists in setting up encrypted wireless connections

---
- Arp-scan
  - Scans IPv4 network for active devices
- Nmap
  - Scans IP for open ports
- Iftop
  - Bandwidth monitor
- Netstat
  - Shows active network connections

---
- Tmux
  - Allows for multiple windows for multitasking in CLI
  - Allows for re-connection to a disconnected session
  - Multi-pane features
- Ssh
  - Secure remote cli sessions
  - Config file allows for easier use
  - Public keys eliminates the need for passwords while remaining secure
  - Scp secure copy

---
- Telnet
  - Similar to ssh
  - Not secure, all in clear text
- Netcat / ncat
  - Network data transfer
- Route
  - Displays and edits routing table
- Resolve.conf
  - DNS servers

---
- Hosts file
  - Can be used as a short-hand for connecting to known servers
  - Can block unwanted sites
- Whatmask / sipcalc
  - Handy tool for identifying subnets and available addresses
- Tftp / ftp / sftp
  - File transfer
- Nfs / showmount
  - Network file sharing, showmount displays available mounts for a server

---
- Samba
  - Windows compatible file sharing
- Vnc
  - Remote desktop / screen sharing
- Unbound / bind / nsd
  - DNS servers and resolvers
- Dhcp server
  - Serves IP addresses to a given network

---
- Openvpn
  - Remote network access
  - Supports encryption
  - Can help with privacy and anonymity